## Slide 1
CAREBAND: Prototype parts & model
Smart assistive wristband • MyBharat Hack for Social Cause
01
What we are building
A wearable that turns selected household sounds into vibration alerts and offers a manual SOS button. Motion-based fall warning, medicine reminders and location sharing are planned add-ons.
ESP32 controller
The controller reads sensor inputs and activates the output.
Microphone / sound sensor
Detects sound level
MPU6050
Measures movement
SOS push button
Manual help request
Vibration motor
Silent wrist alert
ESP32: read → decide → alert
Also required: USB power / suitable battery, jumper wires, breadboard and a wrist strap/case.
Optional upgrades: GPS module + a phone/network connection for remote location alerts.

## Slide 2
How the prototype works
Sensor input → ESP32 processing → vibration or emergency response
02
1. INPUT
Microphone senses sound MPU6050 senses movement SOS button is pressed
2. PROCESS
ESP32 checks programmed rules: sound threshold, motion pattern, or SOS button state
3. OUTPUT
Vibration motor alerts wearer; optional buzzer / LED gives feedback
4. OPTIONAL
Phone/cellular link can send SOS and GPS location to caregiver
Example A — Sound alert
A loud sound is detected → ESP32 triggers a vibration pulse. A basic sensor detects sound level, not necessarily whether it is a cooker or doorbell.
Example B — SOS / possible fall
SOS press triggers a local alert. Motion data can flag a possible fall, but fall detection can make mistakes and needs testing.
Important: GPS alone does not send messages. Remote alerts need a connected phone, Wi-Fi where available, or a cellular module.

## Slide 3
Parts checklist & live demo
Show a working core prototype first; explain other features as future upgrades.
03
Core parts
• ESP32 board • sound sensor / microphone • vibration motor + suitable driver • SOS button • wires / breadboard • power
Optional parts
• MPU6050 for movement • GPS module for location • Buzzer / LED • phone or cellular connection
Demo 1: sound
Play a doorbell sound or clap near the sensor. Show the vibration motor responding.
Demo 2: SOS
Press the SOS button. Show the local alert; only claim remote alerts if tested.
Demo 3: motion
Tilt or move the board by hand to demonstrate sensor readings; do not make anyone actually fall.
Build order
1) Test ESP32 → 2) SOS button → 3) sound-to-vibration → 4) motion sensor → 5) optional phone/GPS.
Safety & accuracy note
This is a student prototype, not a certified medical or emergency device. Test for false alarms.